Προδιαγραφές VPN Router

Για την απομακρυσμένη πρόσβαση στο backbone του Δήμου υπηρεσιών που βρίσκονται εκτός του δικτύου οπτικών ινών, αλλά χρησιμοποιούν ADSL γραμμές θα χρειαστούν VPN routers σύμφωνα με τις παρακάτω προδιαγραφές.

Αφορούν την διασύνδεση 2 σημείων σε πρώτη φάση, ΞΚΓ και την ενότητα Αισωνίας με το ΚΝΤ (κέντρο νέων τεχνολογιών).

Η επέκταση του δικτύου με iNodes, πάνω στα οποία είναι βασισμένη η επικοινωνία των σημείων πρόσβασης στο δίκτυο των οπτικών ινών μέσω Ip Sec πρωτοκόλλου, κρίνεται ασύμφορη, τόσο λόγω του αρχικού κόστους κτίσης όσο και της ετήσιας ανανέωσης των αδειών.

Η τοπολογία του δικτύου μπορεί να περιλαμβάνει τα εγκατεστημένα iNodes ως primary κόμβους και τα VPN routers ως clients θα δίνουν πρόσβαση στα μικρά workgroup (Αισωνία, Αρτέμιδα, Ιωλκός, κλπ).

Με την δημιουργία της παραπάνω υποδομής μας δίνεται η δυνατότητα ενοποίησης όλων σημείων του Δήμου στο volos-city.gr.

Ο προϋπολογισμός των 4 routers (2 για R&D τα οποία θα αποτελούν και backup των σημείων πρόσβασης και 2 για τα σημεία πρόσβασης) είναι 600 ευρώ.

| Α/Α | ΠΕΡΙΓΡΑΦΗ | ΠΡΟΔΙΑΓΡΑΦΕΣ | ΑΠΑΙΤΗΣΗ |
| --- | --- | --- | --- |
|  | Processor | Dual-Core 500 MHz, ή καλύτερος με Hardware Acceleration for Packet Processing | NAI |
|  | System Memory | 512 MB DDR2 RAM ή περισσότερη | NAI |
|  | Onboard Flash Storage | 2 GB ή περισσότερη | NAI |
|  | Layer 3 Forwarding Performance |  |
|  | Packet Size: 512 Bytes or Larger | 3 Gbps (Line Rate) | NAI |
|  | Packet Size: 64 Bytes | 1,000,000 pps | NAI |
|  | Addressing | Static IPv4/IPv6 Addressing DHCP/DHCPv6 | NAI |
|  | Networking Interfaces |  |
|  | Serial Console Port | RJ45 Serial Port | NAI |
|  | Data Ports | 10/100/1000 Ethernet Ports τουλάχιστον 3 | NAI |
|  | Interface/Encapsulation | Ethernet 802.1q VLAN PPPoE GRE IP in IP Bridging Bonding (802.3ad) | NAI |
|  | Routing | Static Routes OSPF/OSPFv3 RIP/RIPng BGP (with IPv6 Support) IGMP Proxy | NAI |
|  | Security | ACL-Based Firewall Zone-Based Firewall NAT | NAI |
|  | QoS | FIFO Stochastic Fairness Queueing Random Early Detection Token Bucket Filter Deficit Round Robin Hierarchical Token Bucket Ingress Policing | NAI |
|  | Services | DHCP/DHCPv6 Server DHCP/DHCPv6 Relay Dynamic DNS DNS Forwarding VRRP RADIUS Client Web Caching PPPoE Server | NAI |
|  | VPN | IPSec Site-to-Site and Remote Access OpenVPN Site-to-Site and Remote Access PPTP Remote Access L2TP Remote Access PPTP Client | NAI |
|  | Management | Web UI CLI (Console, SSH, Telnet) SNMP NetFlow LLDP NTP | NAI |
|  | Certification | CE | NAI |
|  | Εγγύηση (μήνες) | ≥ 12 | NAI |